## Slide 1
MODULE 01 · NOTEBOOK 01_SATELLITE_DATA_EXTRACTION
Reading chlorophyll
and heat from orbit.
Sentinel-2 water quality and Sentinel-3 sea-surface temperature over the Mar Menor — from raw reflectance to the signature of a dying lagoon.
10 m
S2 PIXEL
NDCI
CHL INDEX
+2 °C
2021 HEATWAVE
A·B·C
THREE SECTIONS
MODULE 1 / 00
SATELLITE DATA EXTRACTION · 75 MIN
Notes: Welcome to Module 1. Goal: go from raw satellite data to the visible fingerprints of the Mar Menor's collapse. Two sensors: Sentinel-2 for water colour at 10 m, Sentinel-3 for sea-surface temperature. Stress the three-section structure (A synthetic/offline, B real workflow, C real imagery) — it's how the notebook avoids leaving students stuck.

## Slide 2
§ 01 — WHY THE LAGOON IS HARD
Case-2 waters break the textbook
ocean-colour algorithms.
MODULE 1 / 01
CASE-2 WATERS
Open-ocean (Case-1) algorithms assume phytoplankton alone drives the colour. The Mar Menor is shallow, wind-stirred and nutrient-loaded, so three things confound the signal at once. The fix is the C2RCC neural-network correction, then a locally-calibrated index.
Caveat we state out loud: Sentinel-2 L2A surface reflectance is a LAND correction — not, by itself, an aquatic C2RCC product.
The three confounders
— Suspended sediment raises blue/green → chl-a over-estimated
— CDOM from runoff absorbs in the blue
— Macrophytes on the bottom add a NIR signal
Our chl proxy
— Rrs(B05)/Rrs(B04) — red-edge over red rises with chlorophyll
Notes: The single most important conceptual slide. Explain WHY standard ocean colour fails here: sediment, CDOM and macrophytes each move reflectance independently of chlorophyll. That's the definition of Case-2 water. Then the honesty point: L2A (Sen2Cor) is a land atmospheric correction; for rigorous water work you'd run C2RCC. The proxy B05/B04 exploits the red-edge: chlorophyll absorbs red (B04), reflects red-edge (B05).

## Slide 3
§ 02 — HOW THE NOTEBOOK IS BUILT
Three clearly separated sections.
MODULE 1 / 02
STRUCTURE A·B·C
A · SYNTHETIC
Cached datasets, fully reproducible OFFLINE in class. The 12-point chl-a series and the SST cube. No internet, no account.
B · REAL WORKFLOW
The patterns to discover and download real Sentinel data from CDSE / STAC. Shown, not run in class (needs a free account).
C · REAL IMAGERY
Instructor figures from real Sentinel-2 GeoTIFFs: True-Colour, NDCI, zones. The lagoon outline is the actual satellite coastline.
The split keeps “what runs anywhere” cleanly apart from “what needs the cloud” — so students never get stuck mid-lesson.
Notes: Explain the A/B/C design — it directly answers a reviewer concern that synthetic and real data were visually mixed. Section A always runs (offline). Section B is the real-data recipes (account needed). Section C renders real downloaded imagery and self-skips if the GeoTIFFs aren't present. This is the spine of the whole notebook.

## Slide 4
§ 03 — SECTION A · THE LONG VIEW
Four crises, one chlorophyll curve.
MODULE 1 / 03
CHLOROPHYLL TIME SERIES
Year | Event
2016 | First green-soup crisis — accumulated nitrate
2019 | DANA flood pulse — 300+ mm in 48 h
2021 | August anoxia & fish-kill — the climax
2025 | Bloom resurgence — early-warning test repeats
What the figure shows
— 12 sampling points → lagoon-wide weekly mean
— Documented crises light up in the right months
— Proof the synthetic data is calibrated, not invented
Notes: Section A uses the cached synthetic series. The teaching point: the four documented crises appear at the correct dates and magnitudes because the synthetic generator is calibrated against published literature. Walk the timeline 2016 → 2025. This sets up why 2021 is the focus.

## Slide 5
§ 04 — SECTION A · THE KILL MECHANISM
A marine heatwave that
strangles the oxygen.
MODULE 1 / 04
HEATWAVE → ANOXIA
30.5 °C
AUG 2021 MEAN SST
+1.9 °C
ANOMALY VS CLIMATOLOGY
−0.3 mg/L
O₂ CAPACITY LOST
The chain, quantified
— Warmer water holds less O₂ (Benson–Krause solubility).
— 27.5 → 30.5 °C removes ~0.3 mg/L of oxygen capacity.
— At night the bloom consumes O₂ — and stratification seals the bottom.
— Result: bottom anoxia — the 2021 fish-kill condition.
Teaching point: SST is not a curiosity — it is a computable driver of the ecological collapse.
Notes: The mechanism slide. Make the causal chain explicit and quantitative: a +2 °C heatwave lowers O₂ solubility by ~0.3 mg/L; the bloom respires at night; stratification prevents reoxygenation of the bottom. Together → hypoxia → fish-kill. We show the SST field clipped to the real lagoon outline plus the Benson-Krause O₂ solubility curve.

## Slide 6
§ 05 — SECTION B · HOW TO GET THE DATA
The current Copernicus access path.
MODULE 1 / 05
CDSE · STAC · COG
# Current CDSE STAC endpoint (Nov 2025)
from pystac_client import Client
cat = Client.open(
"https://stac.dataspace.copernicus.eu/v1/")
search = cat.search(
collections=["sentinel-2-l2a"],
datetime="2021-08-01/2021-09-30",
bbox=BBOX,
query={"eo:cloud_cover": {"lt": 20}})
What students must remember
— SciHub is dead; CDSE is the entry point
— New STAC root stac.dataspace.copernicus.eu/v1
— Collection is lowercase sentinel-2-l2a
— Use L2A (surface), not L1C (top-of-atmosphere)
— The COG trick: read only the AOI window, a few MB
Notes: Section B is the real-world recipe — shown, not run in class. The critical correction: the old catalogue.dataspace.copernicus.eu/stac was deprecated Nov 2025; the current root is stac.dataspace.copernicus.eu/v1 and the collection id is lowercase sentinel-2-l2a. Emphasise L2A vs L1C and the cloud-optimised-GeoTIFF window-read trick.

## Slide 7
§ 06 — SECTION C · REAL IMAGERY
Pixel-perfect, from real scenes.
MODULE 1 / 06
TRUE COLOUR · NDCI · ZONES
TRUE COLOUR
Four cloud-free, full-coverage scenes (Feb 2020 → Mar 2022), chosen by measuring real coverage AND cloud over the lagoon — not the catalogue %.
NDCI PER PIXEL
Chlorophyll index over 1.3 M water pixels. Clear winter ≈ −0.28; summer 2021 bloom ≈ −0.05 — a large jump on a shared colour scale.
ZONE ANALYSIS
North / Centre / South medians reveal the gradient driven by agricultural runoff on the north-west shore.
OUTLINE FROM NIR
The lagoon boundary is extracted from the near-infrared band itself — 191 vertices, exact, not a hand-drawn polygon.
Notes: Section C is the visual payoff with real Sentinel-2 pixels. Four key products. Stress two methodological wins: (1) scene selection measures coverage AND cloud over the lagoon — that's why the 14-Jul-2021 swath-edge scene was rejected; (2) the lagoon outline is derived from the NIR band, so borders are pixel-perfect.

## Slide 8
§ 07 — WHAT TO WALK AWAY WITH
Module 1 in four sentences.
1
CDSE, not SciHub. STAC at stac.dataspace.copernicus.eu/v1, collection sentinel-2-l2a.
2
Case-2 means be careful. Atmospheric-correct with C2RCC; never trust raw L2A as an aquatic product.
3
NDCI separates clear water from bloom and exposes the north–south nutrient gradient.
4
A +2 °C heatwave removes ~0.3 mg/L O₂ — enough, with night-time respiration, to drive the 2021 anoxia.
MODULE 1 / 07
FIN · MODULE 1
Notes: Recap and bridge to Module 2: now that we can read the lagoon from space, can we validate it against the buoys and predict the crises with ML?