## Slide 1
MODULE 02 · NOTEBOOK 02_INSITU_TIMESERIES_ML
From buoys to
early warning.
Integrating the in-situ network with the satellite record, validating retrievals, and learning to predict and flag the lagoon's crises.
5
BUOY STATIONS
18k
DAILY RECORDS
2
HONEST CV SCHEMES
42 d
BEST LEAD TIME
MODULE 2 / 00
IN-SITU + MACHINE LEARNING · 70 MIN
Notes: Module 2 connects satellite to ground truth and adds machine learning. Two big honesty themes to flag up front: (1) validate spatially, not just in time; (2) an early-warning detector must be judged out-of-sample. These reflect the review fixes that made the module defensible.

## Slide 2
§ 01 — WHERE THE GROUND TRUTH LIVES
The regional monitoring networks.
MODULE 2 / 01
IN-SITU NETWORKS
CARM MAR MENOR
Real-time sondes around the lagoon: T, S, chl-a, DO, turbidity. The dashboard regional authorities actually watch.
IMIDA / SIAM
Agro-meteorological stations: soil moisture, nitrate proxies — the upstream pressure on the lagoon.
CHS-SAIH
Segura watershed hydrology: precipitation and runoff at 15-minute cadence — the flood signal.
COPERNICUS MARINE INS-TAC
Aggregated in-situ ocean observations (buoys, CTDs, gliders) for the Mediterranean.
Notes: Map the data landscape for in-situ. Our cached buoy file mimics CARM exports: 5 stations, daily, 2016-2025, with T, S, chl-a, turbidity, DO, nitrate. Point out that the upstream (IMIDA/CHS) is what ultimately drives the lagoon — the nutrient pressure.

## Slide 3
§ 02 — THE CRISES IN THE RAW SIGNAL
What the agency saw in real time.
MODULE 2 / 02
HYPOXIA · DANA
August 2021 — the hypoxia
— Dissolved oxygen crashes below 2 mg/L at the worst stations
— SST peaks simultaneously — the heatwave
— This is the plot behind the fish-kill headlines
September 2019 — the DANA
— 300+ mm in 48 h cut-off cold drop
— Salinity drops ~4 PSU as freshwater floods in
— Nitrate spikes ten-fold — the watershed plume
Before any modelling, we simply PLOT the events — the data must show the story we claim to study.
Notes: Exploratory plots first. Show the 2021 DO collapse against the 2 mg/L hypoxia line with SST overlaid, and the 2019 DANA as a precip → nitrate → salinity cascade. Lesson: always eyeball the events before trusting any model on them.

## Slide 4
§ 03 — VALIDATION
Does the satellite agree
with the water?
MODULE 2 / 03
SATELLITE ↔ IN-SITU MATCH-UPS
We co-locate each Sentinel-2 sampling point with its nearest buoy (within 4 km, same day) and score the retrieval the way an ocean-colour paper would. A scatter against the 1:1 line is the honest visual test.
The metrics that matter
— R² — variance explained
— RMSE / RMSLE — error (log form: chl-a is log-normal)
— Bias — systematic over/under-estimate
— 1:1 line on the scatter — the visual truth test
Notes: Match-ups: the discipline of validation. 3 km / 3 h is the ocean-colour convention; we use 4 km / same-day because in-situ is daily. Report R², RMSE, RMSLE (log because chl-a is log-normal) and bias, and always draw the 1:1 line. Never claim skill without a match-up.

## Slide 5
§ 04 — MACHINE LEARNING, DONE HONESTLY
Two cross-validations,
two different questions.
MODULE 2 / 04
GRADIENT BOOSTING · HONEST CV
Scheme | Question it answers | Result
TimeSeriesSplit | Predict future dates? (time order) | high R²
GroupKFold by station | Predict an unseen station? (space) | R² ≈ 0.17
The gap is the lesson: a model that looks great in time can be weak in space. Report the harder number. A gradient-boosting regressor on reflectances + band ratios + season is the workhorse.
Notes: The key ML-rigor slide. TimeSeriesSplit answers 'can I predict future dates' and looks strong. GroupKFold holding out whole stations answers 'can I predict an unmonitored place' and is much harder (R² around 0.17). The honest deployment number is the spatial one. This directly addresses the reviewer's 'too optimistic ML' concern.

## Slide 6
§ 05 — MULTIVARIATE ANOMALY DETECTION
An early-warning detector
that never peeks at the future.
MODULE 2 / 05
ISOLATION FOREST · OUT-OF-SAMPLE
# Fit ONLY on quiet years 2017-18
train = sm.query("date < '2019-01-01'")
iso = IsolationForest(
n_estimators=300,
contamination=0.03,
random_state=42)
iso.fit(train[FEATURES])
# Apply out-of-sample (2019+)
sm['anomaly'] = iso.predict(sm[FEATURES])
Why quiet years only
— Fit on the whole series and it learns the crises as 'normal'
— Train on 2017–2018, apply to 2019+ → every flag is out-of-sample
— Watches chl-a, turbidity, DO, SST, salinity, nitrate jointly
Notes: Anomaly detection with honesty built in. If you fit IsolationForest on all years, the crises become part of 'normal' and the early-warning claim is circular. We fit only on the quiet 2017-18 baseline and apply forward. It's multivariate — joint anomalies across six variables catch precursors a single chl-a threshold misses.

## Slide 7
§ 06 — THE METRIC AGENCIES ACTUALLY WANT
Lead time ≠ detection delay.
MODULE 2 / 06
LEAD TIME VS DELAY
Crisis | First flag | Outcome
2019 DANA | −42 days | genuine early warning
2021 anoxia | +2 days | caught after onset (a miss)
2025 bloom | +1 day | caught after onset (a miss)
We separate a flag BEFORE the start (lead time — the win) from a flag AFTER (detection delay — a miss). Lumping them together is how monitoring papers quietly oversell themselves.
Notes: The subtle but important fix. The naive code scanned a window starting before and ending after the event, took the first flag, and called it 'lead time' — even when it came after onset. We split lead time (before) from detection delay (after). Honest result: 2019 was a real 42-day warning; 2021 and 2025 were caught only after the crisis began.

## Slide 8
§ 07 — WHAT TO WALK AWAY WITH
Module 2 in four sentences.
1
Validate before you model. Match-ups with R²/RMSE/bias and a 1:1 line keep you honest.
2
Time CV and space CV differ. Report the unseen-station score, not just the easy one.
3
Early-warning trains on quiet years and must be judged out-of-sample.
4
Lead time and detection delay are opposites. Only a flag before onset is a real warning.
MODULE 2 / 07
FIN · MODULE 2
Notes: Recap. Bridge to Module 3: Modules 1-2 used data we prepared — Module 3 teaches students to build that data layer themselves.